## Slide 1: Acoustic Source Localization
By: Tiffany Ho, Ajeetpal Dhillon, Harry Nguyen, Andrew Dulaney, Daniel Scarborough, Sidong Guo

## Slide 2: Introduction
Background
  Different Methods
    Time of arrival
    Time difference of arrival
    Receiver signal strength
Objective
  To identify the location of a sound source in a given area.
Motivation
  We would like to make an alternated detection method that offer an alternative approach to video detection.

## Slide 3: Project Description
Localization Software for Acoustic Signals
Motivation
  Applications in Emergency Rescue, child and elderly care
TDOA for Angle
Signal Strength for Distance

## Slide 4: Design Details
MATRIX VOICE
  Circular 8 Mic Array
RASPBERRY PI 3

## Slide 5: Raspberry Pi and Matrix Setup
Two functioning Matrix modules each with a Pi
Pi's can be 3 or 4
  Buster OS
  Matrix HAL Library
Localization.py
  Runs recording executable via subprocess
  Converts .raw files to .wav
  Begins localization algorithm
Documentation on Setup

## Slide 6: Design Specification
Parameters | Specifications
Audio Specification | 8-96 kHz
Bit Depth | Signed 16 bits
Operation Range | 20 meters
Cost | Below $200
Angle Accuracy | Average difference within 3 degrees
Distance Accuracy | Average difference within 30 centimeters
Processing Delay | Average processing delay within half second

## Slide 7: Software Flowchart

## Slide 8: Angle and Distance Calculation
Use multi-condition if statement that compares 4 sets of microphone distance pairs to determine the sector of the source
Calculate 4 angle estimation based on triangulation
Apply sanity check on angle estimates and drop any error estimates, if more than 2 errors are made in 4 angles, drop this acquisition
Apply variance filter to filter outliers, store the angle value
Distance calculated based on RSS, store the RSS value
Ensemble mean averaged over 5 acquisitions in short time period and output the coordinates
Start again for next set of coordinates

## Slide 9: Project Demonstration
Demo of working project
Video for back-up
Will show an overview of GUI
Will test speech/acoustic signals
Will show successful tracking algorithm
GUI will show both actual and expected data

## Slide 10: Schedule, Tasks, & Milestones

## Slide 11: Cost Analysis
Received the Matrix Voice at the cost of $90
Collectively, about 20 hours per week for labor and research
  10 hours for research
  6 hours for algorithm development
  4 hours for GUI research and development
Cost of labor is about $800 to $1,000
  Used a laxed cost of $40 an hour

## Slide 12: Current Status
Algorithm has been translated from MATLAB to Python
  Algorithm can be run repeatedly from executable
  Angle estimation has high accuracy
  RSS model will be established.
GUI team is focused on adding features and interfacing with Algo
  Button functionality has been established
  Graphing predicted vs. real source location is next project goal

## Slide 13: Leadership Roles
1. Tiffany Ho:
  Group leader
  Documentation Coordinator
2. Daniel Scarborough:
  Webmaster
3. Ajeetpal Dhillon:
  Documentation Coordinator
  Hardware/Software Lead
4. Harry Nguyen:
  Financial Manager
  GUI Team Lead
5. Sidong Guo:
  Software/Algorithms Lead
6. Andrew Dulaney:
  Lead for graphing options on GUI